## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors: Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lecture 17:
Jump and loop instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 3 due 10/21
Today’s lecture
  Review
    Compare instructions
    Conditional instructions (CMOVcc, SETcc)
  Jump instructions
  Loop instructions

## Slide 3: Review: compare
CMP D, S
  Flags show result of (D) – (S)
  Result == 0  (D) == (S)
  Result < 0  (D) < (S)
  Result > 0  (D) > (S)
Condition codes: mnemonics implying certain flag conditions

## Slide 4: Review: Condition codes (cont.)
Testing overflow
  O (OF = 1), NO (OF =0)
Testing carry flag
  C (CF = 1)
  NC (CF = 0)
Testing sign flag
  S (SF = 1), NS (SF = 0)
Testing parity flag
  P or PE (PF = 1)
  NP or PO (PF = 0)

## Slide 5: Review: Condition codes (cont.)
Testing equality/zero result
  E or Z (ZF = 1)
  NE or NZ (ZF = 0)
Signed comparison
  L or NGE (SF XOR OF = 1)
  NL or GE (SF XOR OF = 0)
  LE or NG ((SF XOR OF) OR ZF = 1)
  NLE or G ((SF XOR OF) OR ZF = 0)
Unsigned comparison
  “Below”  less than, “above”  greater than
  B, NAE (CF = 1)
  NB, AE (CF = 0)
  BE or NA (CF OR ZF = 1)
  NBE or A (CF OR ZF = 0)

## Slide 6: Review: conditional instructions
Conditional move
  Move performed only if condition is true
  Examples:
    CMOVZ AX, [SI]  move if ZF == 1
    CMOVG EBX, EAX  move if greater than
SETcc D
  Sets single byte destination to 1 (0x01) if condition true; all 0s (0x00) if condition false
  Can be used to build up complex conditions

## Slide 7: Review: SETcc example
Show the results of the following instructions, assuming that
  “A” = (0x100) = 0x0001
  “B” = (0x102) = 0x0003
  “C” = (0x104) = 0x1011
  “D” = (0x106) = 0x1011
  “E” = (0x108) = 0xABCD
  “F” = (0x10A) = 0xDCBA
Tests complex condition:
((A <= B && C == D) || E != F)
MOV AX, [0x100]
CMP AX, [0x102]
SETLE BL
MOV AX, [0x104]
CMP AX, [0x106]
SETE BH
AND BL, BH
MOV AX, [0x108]
CMP AX, [0x10A]
SETNE BH
OR BL, BH

## Slide 8: Jump instructions
Used to change flow of program
  Next instruction specified by operand
Two general types
  Unconditional: JMP <target>
    Always goes to address indicated by <target>
  Conditional: Jcc <target>
    Jump only occurs if condition true
    cc replaced by valid condition code
      Most codes discussed in previous lecture
      Additional codes: CXZ/ECXZ
       CX/ECX register is zero

## Slide 9: Jump Instructions

## Slide 10: Example: program structure 1
Given the instructions below, what are the resulting register values if:
  AX = 0x0010, BX = 0x0010
  AX = 0x1234, BX = 0x4321
What type of high-level program structure does this sequence demonstrate?
Instructions
  CMP AX, BX
  JE L1
  ADD AX, 1
  JMP L2
  L1: SUB AX, 1
  L2: MOV [0x100], AX

## Slide 11: Example solution
First case: AX = BX = 0x0010
  CMP AX, BX  Shows AX == BX
  JE L1  Cond. true—jump to L1
  ADD AX, 1
  JMP L2
  L1: SUB AX, 1  AX = AX – 1 = 0x000F
  L2: MOV [0x100], AX  Store 000F at 0x100

## Slide 12: Example solution (cont.)
Second case: AX = 0x1234, BX = 0x4321
  CMP AX, BX  Shows AX < BX
  JE L1  Cond. false—no jump
  ADD AX, 1  AX = AX + 1 = 0x1235
  JMP L2  Unconditional jump to L2
  L1: SUB AX, 1
  L2: MOV [0x100], AX  Store 0x1235 at 0x100

## Slide 13: Example solution (cont.)
High-level program structure: if/else statement
  If part: compare + jump (if (AX == BX))
  Else part: what follows if condition false
  Unconditional jump used to skip “if” part
  Both parts have same exit (L2)

## Slide 14: Example: program structure 2
Given the instructions below, what are the resulting register values if, initially, AX = 0x0001?
What type of high-level program structure does this sequence demonstrate?
Instructions
  MOV CL, 5
  L: SHL AX, 1
  DEC CL
  JNZ L

## Slide 15: Example solution
  MOV CL, 5  CL = 5
  L: SHL AX, 1  AX: 1  2  4  8  16  32
  DEC CL  CL: 5  4  3  2  1  0
  JNZ L  Jumps to L as long as CL ≠ 0
Overall structure: loop
  Essentially a for loop: for (CL = 5; CL != 0; CL--)
  For loops are technically pre-tested (loop condition checked at start of each iteration)
    No difference between end of one iteration and start of next
    We know condition is true in first iteration—5 ≠ 0

## Slide 16: Example: program structure 3
Given the instructions below, what are the resulting register values if, initially, AX = 0x0001?
What type of high-level program structure does this sequence demonstrate?
Instructions
  MOV CX, 5
  L: JCXZ END
  ADD AX, AX
  DEC CX
  JMP L
  END: MOV [0x10], AX

## Slide 17: Example solution
  MOV CX, 5  CX = 5
  L: JCXZ END  Jumps to “END” when CX = 0
  ADD AX, AX  AX: 1  2  4  8  16  32
  DEC CX  CX: 5  4  3  2  1  0
  JMP L
  END: MOV [0x10], AX

## Slide 18: Loop instructions
Common operations in basic loops
  Compare
  Conditional jump
  Decrement loop counter (CX)
Loop instructions combine all into one op
  All decrement CX by 1, then check if CX == 0
  <target> must be short-label (8-bit immediate)
  LOOP <target>: Return to <target> if CX != 0
  LOOPE/LOOPZ <target>: Return to <target> if
  (CX != 0) && (ZF == 1)
  LOOPNE/LOOPNZ <target>: Return to <target> if (CX != 0) && (ZF != 1)

## Slide 19: Loop example 1
Rewrite the post-tested loop seen earlier using a loop instruction:
  MOV CL, 5
  L: SHL AX, 1
  DEC CL
  JNZ L
Solution:
  MOV CL, 5
  L: SHL AX, 1
  LOOP L

## Slide 20: Loop example 2
Describe the operation of the following program (Example 6.15-6.16).
What is the final value of ESI if the 15 bytes between 0x0A001 and 0x0A00F have the following values?
  00 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E
MOV DL, 05
MOV EAX, 0x0000A000
MOV ESI, 0
MOV CX, 0x000F
AGAIN:INC SI
CMP [EAX + ESI], DL
LOOPNE AGAIN

## Slide 21: Final notes
Next time:
  Subroutines
Reminders:
  HW 3 due 10/21