## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors: Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lecture 6:
Assembly basics
Data transfer instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 1 due today (9/16)
    Submit work via Blackboard
    Can handwrite solution but must scan all pages and combine into single document
      Word doc or PDF, no archive files
  HW 2 to be posted; due Monday, 9/23
Lecture topics
  Assembly basics
  Data transfer instructions

## Slide 3: Instruction Assembly Notation
Each instruction is represented by a mnemonic that describes its operation—called its operation code (opcode)
  MOV = move (data transfer)
  ADD = add (arithmetic)
  AND = logical AND (logic)
  JMP = unconditional jump (control transfer)
Operands are the other parts of an assembly language instructions
    Identify whether the elements of data to be processed are in registers or memory
      Source operand– location of one operand to be processed
      Destination operand—location of the other operand to be processed and the location of the result

## Slide 4: Assembly Language Statements
General structure of an assembly language statement
LABEL: INSTRUCTION ;COMMENT
  Label—address identifier for the statement
  Instruction—the operation to be performed
  Comment—documents the purpose of the statement
  Example:
START: MOV AX, BX ; Copy BX into AX
Other examples:
  INC SI ;Update pointer
ADD AX, BX
  Few instructions have a label—usually marks a jump to point
  Not all instructions need a comment

## Slide 5: x86 memory accesses
# bytes from memory usually = # bytes in register
Example: MOV AX, [0x100]
  AX is 16-bit register  copy word from address 0x100 to AX
Sometimes necessary to specify size
  Use “<size> PTR”: BYTE PTR, WORD PTR, DWORD PTR
  Example: MOVZX EAX, BYTE PTR [0x100]
    Take byte from memory
    Zero-extend data to 32 bits and store in EAX
Remember, x86 uses little-endian data

## Slide 6: Data transfer instructions
MOV
MOVSX
MOVZX
XCHG
LEA
Additional data transfer instructions (covered later, if at all)
  Load full pointer (segmented addressing)
  PUSH/POP (stack transfers)
  INS/OUTS (I/O)
  MOVS/LODS/STOS (string instructions)
  BSWAP (switch from little endian to big endian)
  XLAT (table lookup)
  CMOV (conditional move)

## Slide 7: MOV
Used to copy data between
  Registers
  Registers/memory
  Immediate value (source only) to register/memory
Format: MOV D, S
Operation: (D) = (S)
Immediate value can only be used as source

## Slide 8: MOV examples
Assume: AX = 0x0100, SI = 0x3000,
(0x100) = 0x00, (0x101) = 0xFF
MOV BL, AL
  BL = AL = 0x00
MOV DX, SI
  DX = SI = 0x3000
MOV CX, [0x100]
  CX = word starting at 0x100 = 0xFF00

## Slide 9: Usage of Move Instruction
Example—Initialization of internal registers with immediate data and address information
  What is the final state of all affected registers?
MOV AX, 0
MOV BX, AX
MOV CX, 0x0A
MOV DX, 0x100
MOV SI, 0x200
MOV DI, 0x300

## Slide 10: Usage of Move Instruction (soln)
MOV AX, 0  AX = 0x0000
MOV BX, AX  BX = AX = 0x0000
MOV CX, 0x0A  CX = 0x000A
MOV DX, 0x100  DX = 0x0100
MOV SI, 0x200  SI = 0x0200
MOV DI, 0x300  DI = 0x0300

## Slide 11: MOVSX/MOVZX
Move and extend data (fill upper bits with 0/1)
  ZX  zero extend
  SX  sign extend  copy MSB of source
Format: MOVZX D, S
MOVSX D, S
Operation: lower bits of D = S
upper bits of D = 0 (MOVZX) or
upper bits of D = MSB of S (MOVSX)
Restrictions
  Only register/memory operands (no immediates)
  Source must contain fewer bits than destination
  If memory operand used, size must be specified

## Slide 12: MOVSX/MOVZX examples
Assume: AX = 0x0100, DX = 0x8100,
(0x100) = 0x00, (0x101) = 0xFF
What are the results of the following instructions?
MOVSX EBX, AX
MOVSX EBX, DX
MOVZX EBX, DX
MOVSX EBX, BYTE PTR [0x100]
MOVSX EBX, WORD PTR [0x100]

## Slide 13: MOVSX/MOVZX examples (soln)
Assume: AX = 0x0100, DX = 0x8100,
(0x100) = 0x00, (0x101) = 0xFF
What are the results of the following instructions?
MOVSX EBX, AX
  EBX = AX sign-extended = 0x00000100 (orig. value underlined)
MOVSX EBX, DX
  EBX = DX sign-extended = 0xFFFF8100
MOVZX EBX, DX
  EBX = DX zero-extended = 0x00008100
MOVSX EBX, BYTE PTR [0x100]
  EBX = byte at 0x100 sign-extended = 0x00000000
MOVSX EBX, WORD PTR [0x100]
  EBX = word at 0x100 sign-extended = 0xFFFFFF00

## Slide 14: XCHG
Swap contents of source and destination
Format: XCHG D, S
Operation: (D) = (S)
(S) = (D)
Restrictions:
  Memory operand can only be used as destination

## Slide 15: LEA
Perform effective address computation and store result in register
  This instruction looks like a memory access, but does not access memory
Format: LEA D, EA
Operation: D = EA
Example: LEA SI, [0x10 + DI]
  SI = 0x10 + DI

## Slide 16: Example
 | Lo |  |  | Hi
0x528000 | 50 | 88 | 31 | A3
0x528004 | B2 | FF | 0F | 7D
0x528008 | 07 | D0 | BE | 22
0x52800C | 11 | 96 | 00 | 14
Given the initial memory contents at left, show the results of the following instruction sequence:
MOV EAX, 0x528000
MOV EBX, [EAX+2]
XCHG BL, BH
LEA EDX, [EAX+8]
MOV ECX, [EDX-3]

## Slide 17: Solution
MOV EAX, 0x528000
EAX = 0x528000
MOV EBX, [EAX+2]
EBX = DWORD at 0x528002 = 0xFFB2A331
XCHG BL, BH
Swap BL and BH  EBX = 0xFFB231A3
LEA EDX, [EAX+8]
EDX = EAX+8 = 0x528008
MOV ECX, [EDX-3]
ECX = DWORD at 0x528005 = 0x077D0FFF

## Slide 18: Final notes
Next topics:
  Arithmetic instructions
Reminders:
  HW 1 due today (9/16)
    Submit work via Blackboard
    Can handwrite solution but must scan all pages and combine into single document
      Word doc or PDF, no archive files
  HW 2 to be posted; due Monday, 9/23