## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger and Dr. Lin Li
Fall 2019
Lecture 8:
Arithmetic instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 2 due on Wednesday (9/25)
  Exam 1: Monday, 9/30
    Will provide list of instructions
    Will be allowed one, double-sided 8.5” x 11” note sheet
    Will be allowed calculator; no other electronic devices
Review
  Data transfer instructions (XCHG, LEA)
Today’s lecture
  Arithmetic instructions

## Slide 3: Review: XCHG, LEA
XCHG: swap contents of source, dest
  For example, if AX = 0x1234 and BX = 0x5678:
  XCHG AX, BX  AX = 0x5678, BX = 0x1234
LEA: load effective address
  Store result of effective address computation in register
  Instruction doesn’t actually access memory
  For example, given AX = 0x3170:
  LEA CX, [AX+0x0220]  CX = 0x3390

## Slide 4: Example
 | Lo |  |  | Hi
0x528000 | 50 | 88 | 31 | A3
0x528004 | B2 | FF | 0F | 7D
0x528008 | 07 | D0 | BE | 22
0x52800C | 11 | 96 | 00 | 14
Given the initial memory contents at left, show the results of the following instruction sequence:
MOV EAX, 0x528000
MOV EBX, [EAX+2]
XCHG BL, BH
LEA EDX, [EAX+8]
MOV ECX, [EDX-3]

## Slide 5: Solution
MOV EAX, 0x528000
EAX = 0x528000
MOV EBX, [EAX+2]
EBX = DWORD at 0x528002 = 0xFFB2A331
XCHG BL, BH
Swap BL and BH  EBX = 0xFFB231A3
LEA EDX, [EAX+8]
EDX = EAX+8 = 0x528008
MOV ECX, [EDX-3]
ECX = DWORD at 0x528005 = 0x077D0FFF

## Slide 6: Flags
All arithmetic instructions set flags
  CF = carry flag (carry output from MSB of add/sub)
  OF = overflow flag
  ZF = zero flag (result is zero)
  SF = sign flag (1 if negative, 0 if positive)
  PF = parity flag (even parity in LSB)
  AF = auxiliary carry (carry between nibbles)
Stored in FLAGS register
Referenced in conditional instructions

## Slide 7: Addition instructions
ADD D, S
  Operation: (D) = (D) + (S)
ADC D, S
  Operation: (D) = (D) + (S) + (CF)
INC D
  Operation: (D) = (D) + 1

## Slide 8: Subtraction instructions
SUB D, S
  Operation: (D) = (D) – (S)
SBB D, S
  Operation: (D) = (D) – (S) – (CF)
DEC D
  Operation: (D) = (D) – 1
NEG D
  Operation: (D) = -(D)
  Two’s complement negation

## Slide 9: Addition/subtraction examples
Given the following initial state:
  AX = 0x1234
  BL = 0xAB
  Memory location SUM = 0x00CD
Show the results of each step of the following instruction sequence:
  ADD AX, [SUM]
  ADC BL, 0x05
  NEG BL
  SUB AX, 0x12
  INC WORD PTR [SUM]

## Slide 10: Example solution
ADD AX, [SUM]
  AX = (SUM) + AX
  0x00CD + 0x1234 = 0x1301
  AX = 0x1301, CF = 0
ADC BL, 0x05
  BL = BL + 0x05 + CF
  0xAB + 0x05 + 0 = 0xB0
  BL = 0xB0, CF = 0
NEG BL
  BL = –BL
  –0xB0 = –(1011 0000)2 = 0101 00002 = 0x50

## Slide 11: Example solution (cont.)
SUB AX, 0x12
  AX = AX – 0x0012
  0x1301 – 0x0012 = 0x12EF
  AX = 0x12EF, CF = 0
INC WORD PTR [SUM]
  (SUM) = (SUM) + 1
  0x00CD + 1 = 0x00CE
  (SUM) = 0x00CE, CF = 0

## Slide 12: Multiplication/division
Both signed and unsigned integer versions
Register A is always one of the sources
Destination always same; size-dependent
  Exception: signed multiplication does allow for slightly different operation
Easiest way to evaluate instructions: figure out decimal values of operands, do operation in decimal, then figure out binary/hex values of results

## Slide 13: MUL/IMUL
MUL S  unsigned multiplication
IMUL S  signed multiplication
Byte: (AX) = (AL) * (S)
Word: (DX,AX) = (AX) * (S)
Double-word: (EDX,EAX) = (EAX) * (S)
Only CF, OF updated
  If upper half of result = 0, CF & OF = 0
  Otherwise, CF & OF = 1

## Slide 14: DIV/IDIV
DIV S  unsigned division
IDIV S  signed division
Result split into quotient, remainder
Byte: (AL) = (AX) / (S)
(AH) = (AX) % (S)
Word: (AX) = (DX,AX) / (S)
(DX) = (DX,AX) % (S)
Dword: (EAX) = (EDX,EAX) / (S)
(EDX) = (EDX,EAX) % (S)
Special “convert” instructions used to sign-extend value in register A before division
Flags undefined
  Overflow causes exception

## Slide 15: Example
Given
  EAX = 0x00000005
  EBX = 0x0000FF02
What are the results of the following instructions? (Assume all instructions start with same values in registers above)
  MUL BL
  MUL BH
  IMUL BH
  DIV BL
  DIV BH
  IDIV BH

## Slide 16: Solution
Consider that BH = 0xFF = 1111 11112
  As unsigned value, 0xFF = 25510
  As signed value, 0xFF = -110
MUL BL
  AX = AL * BL = 0x05 * 0x02 = 5 * 2 = 1010 = 0x000A
MUL BH
  Unsigned multiplication
  AX = AL * BH = 0x05 * 0xFF = 5 * 255 = 127510
  = 0x04FB
IMUL BH
  Signed multiplication
  AX = AL * BH = 0x05 * 0xFF = 5 * -1 = -510 = 0xFFFB

## Slide 17: Solution (continued)
Consider that BH = 0xFF = 1111 11112
  As unsigned value, 0xFF = 25510
  As signed value, 0xFF = -110
DIV BL
  AL = AX / BL = 0x0005 / 0x02 = 5 / 2 = 0x02
  AH = AX % BL = 0x0005 % 0x02 = 5 % 2 = 0x01
DIV BH
  Unsigned division
  AL = AX / BH = 0x0005 / 0xFF = 5 / 255 = 0x00
  AH = AX % BH = 0x0005 / 0xFF = 5 % 255 = 0x05
IDIV BH
  Signed division
  AL = AX / BH = 0x0005 / 0xFF = 5 / -1 = -5 = 0xFB
  AH = AX % BH = 0x0005 % 0xFF = 5 % -1 = 0x00

## Slide 18: Multiplication/division
Both signed and unsigned integer versions
Register A is always one of the sources
Destination always same; size-dependent
  Exception: signed multiplication does allow for slightly different operation
Easiest way to evaluate instructions: figure out decimal values of operands, do operation in decimal, then figure out binary/hex values of results

## Slide 19: MUL/IMUL
MUL S  unsigned multiplication
IMUL S  signed multiplication
Byte: (AX) = (AL) * (S)
Word: (DX,AX) = (AX) * (S)
Double-word: (EDX,EAX) = (EAX) * (S)
Only CF, OF updated
  If upper half of result = 0, CF & OF = 0
  Otherwise, CF & OF = 1

## Slide 20: DIV/IDIV
DIV S  unsigned division
IDIV S  signed division
Result split into quotient, remainder
Byte: (AL) = (AX) / (S)
(AH) = (AX) % (S)
Word: (AX) = (DX,AX) / (S)
(DX) = (DX,AX) % (S)
Dword: (EAX) = (EDX,EAX) / (S)
(EDX) = (EDX,EAX) % (S)
Special “convert” instructions used to sign-extend value in register A before division
Flags undefined
  Overflow causes exception

## Slide 21: Example
Given
  EAX = 0x00000005
  EBX = 0x0000FF02
What are the results of the following instructions? (Assume all instructions start with same values in registers above)
  MUL BL
  MUL BH
  IMUL BH
  DIV BL
  DIV BH
  IDIV BH

## Slide 22: Solution
Consider that BH = 0xFF = 1111 11112
  As unsigned value, 0xFF = 25510
  As signed value, 0xFF = -110
MUL BL
  AX = AL * BL = 0x05 * 0x02 = 5 * 2 = 1010 = 0x000A
MUL BH
  Unsigned multiplication
  AX = AL * BH = 0x05 * 0xFF = 5 * 255 = 127510
  = 0x04FB
IMUL BH
  Signed multiplication
  AX = AL * BH = 0x05 * 0xFF = 5 * -1 = -510 = 0xFFFB

## Slide 23: Solution (continued)
Consider that BH = 0xFF = 1111 11112
  As unsigned value, 0xFF = 25510
  As signed value, 0xFF = -110
DIV BL
  AL = AX / BL = 0x0005 / 0x02 = 5 / 2 = 0x02
  AH = AX % BL = 0x0005 % 0x02 = 5 % 2 = 0x01
DIV BH
  Unsigned division
  AL = AX / BH = 0x0005 / 0xFF = 5 / 255 = 0x00
  AH = AX % BH = 0x0005 / 0xFF = 5 % 255 = 0x05
IDIV BH
  Signed division
  AL = AX / BH = 0x0005 / 0xFF = 5 / -1 = -5 = 0xFB
  AH = AX % BH = 0x0005 % 0xFF = 5 % -1 = 0x00

## Slide 24: Final notes
Next time:
  Exam 1 Preview (Friday, 9/27)
Reminders:
  HW 2 due on Wednesday (9/25)
  Exam 1: Monday, 9/30
    Will provide list of instructions
    Will be allowed one, double-sided 8.5” x 11” note sheet
    Will be allowed calculator; no other electronic devices