## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors: Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lectures 2 & 3:
Data storage and addressing

## Slide 2: Lecture announcements
HW 1 due Monday, 9/16
  Submit work via Blackboard
  Can handwrite solution but must scan all pages and combine into single document
    Word doc or PDF, no archive files

## Slide 3: Lecture outline
Instruction set architecture
Data types
Data storage
  Storage media
  Alignment
  Endianness
Addressing modes
These slides will cover next 2-3 lectures

## Slide 4: Processor architecture
“Architecture” can refer to
  High-level description of hardware; could be
    Overall system
    Microprocessor
    Subsystem within processor
  Operations available to programmer
    Instruction set architecture
  Other applications to computing (e.g., “software architecture”) we won’t discuss
Commonly used to discuss functional units and how they work together

## Slide 5: Role of the ISA
User writes high-level language (HLL) program
Compiler converts HLL program into assembly for the particular instruction set architecture (ISA)
Assembler converts assembly into machine language (bits) for that ISA
Resulting machine language program is loaded into memory and run

## Slide 6: Abstraction of program control
Easiest for humans to understand high-level languages
Processor interprets machine language
Assembly language: abstraction with intermediate level of detail
  Breaks machine code into instructions
  Gives some insight into how each instruction behaves
  More readable than bit patterns!

## Slide 7: ISA design
Think about a HLL statement like
X[i] = i * 2;
ISA defines how such statements are translated to machine code
  What information is needed?

## Slide 8: ISA design (cont.)
Think about a HLL statement like
X[i] = i * 2;
Questions answered in every ISA (or “software model”)
  How will the processor implement this statement?
    What operations are available?
    How many operands does each instruction use?
  Where are X[i] and i?
    How do we reference the operands?
  What type(s) of data are X[i] and i?
    What types of operands are supported?
    How big are those operands?
  Instruction format issues
    How many bits per instruction?
    What does each bit or set of bits represent?
    Are all instructions the same length?

## Slide 9: Operation types
Operations: what should processor be able to do?
  Data transfer
    Move data between storage locations
  Arithmetic operations
    Typical: add, subtract, maybe multiply/divide, negation
  Logical operations
    Typical: AND, OR, NOT, XOR
    Often includes bit manipulation: shifts, rotates, test/set/clear single bit
  Program control
    “Jump” to another part of program
    May be based on condition
    Used to implement loops, conditionals, function call/return
  Typically some processor-specific special purpose ops

## Slide 10: Operands
Two major questions when dealing with data
  “How” do we store them?  what do the bits represent?
  Where do we store them?
    … and how do we access those locations?
First question deals with data types
Second question deals with data storage and addressing

## Slide 11: Data types
Also seen in high-level languages
  Think about C types: int, double, char, etc.
  What does a data type specify?
    How big is each piece of data?
    How do we interpret the bits representing those data?
Data sizes
  Smallest addressable unit: byte (8 bits)
  Can also deal with multi-byte data: 16, 32, 64 bits
  Often deal with words of data
    Word size processor-dependent (16 bits on x86, 32 bits on MIPS)
    Can have double words, quad words, half words …
Interpreting bits
  Numbers: Integers, floating-point; signed vs. unsigned
  May treat as characters, other special formats

## Slide 12: Unsigned Integers
Types:
Sizes Range
8-bit 0H  25510
16-bit 0H  65,53510
32-bit 0H  4,294,967,29510

## Slide 13: Signed Integers
MSB is sign bit ( 0/1 -> +/-)
Remaining bits represent value
Negative numbers expressed in 2’s complement notation
Types:
Sizes Range
8-bit -128  +127
16-bit -32,768  +32,767
32-bit -2,147,483,648  +2,147,483,647

## Slide 14: Integer Examples
Given the 8-bit value: 1001 11112
Calculate the decimal value of this integer as
  An unsigned integer
  A signed integer

## Slide 15: Integer example solution
Given the 8-bit value: 1001 11112
Calculate the decimal value of this integer as
  An unsigned integer
  Solution:
    (1 x 27) + (1 x 24) + (1 x 23) + (1 x 22) + (1 x 21) + (1 x 20)
    = 128 + 16 + 8 + 4 + 2 + 1 = 159
  A signed integer
  Solution:
    MSB = 1  negative value
    To get magnitude, take 2’s complement:
    0110 00012 = (1 x 26) + (1 x 25) + (1 x 20)
    = 64 + 32 + 1 = 97
     Result = -97

## Slide 16: Floating-point Numbers
Floating-point data stored in two parts
  Significand (fraction)
  Exponent
Single-precision (32 bits) or double-precision (64 bits)

## Slide 17: Data storage
What characteristics do we want storage media to have?
Two primary answers
  Speed
  Capacity
  Very difficult to get both in single storage unit
Processors use two different types of storage
  Registers
  Memory

## Slide 18: Registers
Small, fast set of storage locations close to processor core (execution engine)
Primarily used for computation, short-term storage
  Speed  ideal for individual operations
  Lack of capacity  will frequently overwrite
Reference registers by name
  Example: ADD EAX, EBX  EAX = EAX + EBX
  EAX, EBX are registers in x86 architecture

## Slide 19: Memory
Provides enough capacity for all code, data (possibly I/O as well)
Typically organized as hierarchy
Used primarily for long-term storage
  Lacks speed of registers
  Provides capacity to ensure data not overwritten
Reference memory by address
  Example: MOV EAX, [100h]
   EAX = memory at address [100h]

## Slide 20: Memory (continued)
Accessing single byte is easy
Considerations with multi-byte data
  Are the data aligned?
    Easier/faster to access aligned data
  How are the data organized in memory (“endianness”)?
    Given 32-bit number: DEADBEEFh or 0xDEADBEEF
    Which byte—MSB (0xDE) or LSB (0xEF) gets stored in memory first?

## Slide 21: Aligned Words, Double words
Aligned data: address is divisible by # of bytes
  2 bytes  address must be even
  4 bytes  address must be multiple of 4
x86 architecture doesn’t require aligned data access
  Performance impact for accessing unaligned data in memory (32-bit data bus)
Byte address |  |  |  |  | 
0 |  |  |  |  | 
4 |  |  |  |  | 
8 |  |  |  |  | 
12 |  |  |  |  | 
16 |  |  |  |  | 
20 |  |  |  |  | 
Aligned word
Aligned double word
Unaligned
word
Unaligned
double
word

## Slide 22: Byte order (“endianness”)
In a multi-byte operand, how are the bytes ordered in memory?
Assume the double word value 1,000,000 (0x000F4240) is stored at address 80
  In a little-endian ISA (like x86), the least significant byte (the “little” end) is at address 80
  In a big-endian ISA (like MIPS), it’s the other way around
 |  | 00 | 0F | 42 | 40 |  | 
… | 79 | 80 | 81 | 82 | 83 | 84 | …
 |  | 40 | 42 | 0F | 00 |  | 
… | 79 | 80 | 81 | 82 | 83 | 84 | …

## Slide 23: Examples
Given the following memory contents:
  Starting address of each line shown on left
  Leftmost byte has lowest address
    First line: addresses 0x200C, 0x200D, 0x200E, 0x200F
What is the value of:
  The word starting at address 0x200D?
  The double word starting at address 0x2012?
Are these data aligned?
 | Lo |  |  | Hi
0x200C | 40 | 96 | 2C | 00
0x2010 | 55 | 12 | CD | AB
0x2014 | 01 | 23 | 88 | 99

## Slide 24: Solution
Word at 0x200D = 0x2C96
  Address is not divisible by 2  unaligned
Double word at 0x2012 = 0x2301ABCD
  Address is not divisible by 4  unaligned
    Remember, hexadecimal is base 16—0x12 = 1810
 | Lo |  |  | Hi
0x200C | 40 | 96 | 2C | 00
0x2010 | 55 | 12 | CD | AB
0x2014 | 01 | 23 | 88 | 99

## Slide 25: Addressing modes
Addressing modes: ways of specifying operand location
Where are operands stored? (3 location types)
  Registers  register addressing
    Provide name of register; value read from register
  Memory
    Provide address in memory; value read from that location
    Several modes for specifying memory address
  In the instruction  immediate addressing

## Slide 26: Memory addressing
Instructions accessing memory generate effective address (EA)
  Address calculated as part of instruction
  EA can be used as
    Actual memory address in a simple memory system
    Address within a particular segment in a segmented memory architecture
Effective address calculations can involve
  A constant value
  One or more values stored in registers
  Some combination of register and constant

## Slide 27: General memory addressing modes
Memory direct addressing
  EA = constant value encoded in instruction
Register indirect addressing
  EA = value stored in register
Base + displacement addressing
  EA = constant displacement + base register(s)
  Can have variations of this mode based on number and type of registers
Scaled addressing
  EA = base + (scale * index)
  Used for array addressing

## Slide 28: Final notes
Next time:
  x86 introduction
Reminders:
  HW 1 due Monday, 9/16
    Submit work via Blackboard
    Can handwrite solution but must scan all pages and combine into single document
      Word doc or PDF, no archive files