## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors: Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lecture 4:
x86 intro

## Slide 2: Lecture outline
Announcements/reminders
  HW 1 due Monday, 9/16
    Submit work via Blackboard
    Can handwrite solution but must scan all pages and combine into single document
      Word doc or PDF, no archive files
Today’s lecture
  x86 introduction
  x86 memory accesses

## Slide 3: x86 intro
“x86”  family of general purpose Intel processors
  Starts with 8086 processor (1978)
  Used (w/extensions) in current processors
Supports use of 8, 16, 32, or 64 bit data
  “IA-32”: x86 for 32-bit processors (80386 and later)
  “x86-64”: x86 with 64-bit extensions (AMD, Intel, VIA)
  “IA-64”: old name for Itanium server architecture (not extension of x86)
Allows both register and memory operands
Segmented or flat memory architecture
Real and protected mode operation
  Protected mode supports virtual memory

## Slide 4: Register Set
Nine 32-bit registers
  Data registers- EAX, EBX, ECX, EDX, can be used as 32, 16 or 8bit
  Pointer registers- EBP, ESP
  Index registers- ESI, EDI
  Instruction pointer- EIP (not shown)
Flags (status) register-EFLAGS (not shown)
Source: http://www.cs.virginia.edu/~evans/
cs216/guides/x86.html

## Slide 5: Register Set
64-bit extensions added with Pentium 4
  Data/pointer/index/IP/ flag register extended to 64 bits
  For example:
    RAX = 64-bit register A
    RSP = 64-bit stack pointer
  8 additional data registers (R8-R15)

## Slide 6: General Purpose Data Registers
Four general purpose data registers
  Accumulator (A) register
  Base (B) register
  Count (C) register
  Data (D) register
Can hold 8-bit, 16-bit, or 32-bit data
  AH/AL = high and low byte value
  AX = word value
  EAX = double word value
General uses:
  Hold data such as source or destination operands for most operations—ADD, AND, SHL
  Hold address pointers for accessing memory
Some also have dedicated special uses
  C—count for loop,
  B—table look-up translations, base address
  D—indirect I/O and string I/O

## Slide 7: Pointer/Index Registers
Two pointer registers (32-/16-bit versions)
  Stack pointer register (ESP/SP)
    Points to top of stack
  Base pointer register (EBP/BP)
    Points to fixed location within current stack frame
Two index registers
  Source index (ESI/SI)
  Destination index (EDI/DI)
  Typically used in memory addressing

## Slide 8: Flags Register
32-bit register holding single bit status and control information
9 active flags in real mode
Two categories
  Status flags: conditions resulting from instruction
    Most instructions update status
    Used as test conditions
  Control flags: control processor functions
    Used by software to turn on/off operating capabilities

## Slide 9: x86 memory spaces
x86 architecture implements independent memory and input/output (not shown) address spaces
Memory address space
  1 MB “real” memory
    System + transient program area (TPA)
  Extended memory size dependent on processor
Input/output address space- 65,536 bytes long (64KB)

## Slide 10: x86 memory modes
Two general modes of access
  Real mode (DOS)
  Protected mode (Windows)
Two memory models
  Segmented memory model
  Flat memory model
    We’ll use this model

## Slide 11: Flat mode addressing
No segmentation
  Entire address space active
Address generated by instruction = linear address being accessed
Generates 40-bit external address

## Slide 12: x86 addressing modes
Addresses in x86 instructions enclosed by brackets
Addressing modes: all examples of general addressing modes discussed earlier
Direct addressing
  EA = constant value
  Example: MOV AX, [0x0100]
Register indirect addressing
  EA = value stored in register
  Example: MOV [EDI], AX
Base-plus-index addressing
  EA = sum of two registers
  Example: MOV AX, [EBX+ESI]

## Slide 13: x86 addressing modes (cont.)
Register relative addressing
  EA = register + constant
  Examples:
    MOV CL, [EBX+4]
    MOV AX, ARRAY[EBX] ARRAY is constant memory location
Base relative-plus-index addressing
  EA = base register + index register + constant
  Example: MOV AX, 0x10[ESI][EBX] -or-
  MOV AX, [0x10+SI+BX]
Scaled-index addressing
  EA = register + (scaling factor * second register)
  Often useful for array accesses
    Scaling factor = element size (2, 4, 8 bytes)
  Example: MOV EDX, [EAX + 4*EBX]

## Slide 14: Example
Compute the address for the memory operand in each of the following instructions.
  You do not need to specify what data is transferred
The register contents and variables are as follows:
  (ESI) = 0x00000100
  (EDI) = 0x00000200
  (EBX) = 0x00000300
MOV [EBX+0x0400], CX
MOV [EDI+2*EBX], AH
MOV [EBX+EDI+0x0400], AL

## Slide 15: Example solutions
Memory operand in: MOV [EBX+0x0400], CX
  Addr = value in EBX + 0x0400
  = 0x00000300h + 0x0400 = 0x00000700
Memory operand in: MOV [EDI+2*EBX], AH
  Addr = value in EDI + 2 * value in EBX
  = 0x00000200 + 2 * 0x00000300
  = 0x00000200 + 0x00000600 = 0x00000800
Memory operand in MOV [EBX+EDI+0400h], AL
  Addr = EBX + EDI + 0x0400
  = 0x00000300 + 0x00000200 + 0x0400
  = 0x00000900

## Slide 16: Instruction Assembly Notation
Each instruction is represented by a mnemonic that describes its operation—called its operation code (opcode)
  MOV = move (data transfer)
  ADD = add (arithmetic)
  AND = logical AND (logic)
  JMP = unconditional jump (control transfer)
Operands are the other parts of an assembly language instructions
    Identify whether the elements of data to be processed are in registers or memory
      Source operand– location of one operand to be processed
      Destination operand—location of the other operand to be processed and the location of the result

## Slide 17: Assembly Language Statements
General structure of an assembly language statement
LABEL: INSTRUCTION ;COMMENT
  Label—address identifier for the statement
  Instruction—the operation to be performed
  Comment—documents the purpose of the statement
  Example:
START: MOV AX, BX ; Copy BX into AX
Other examples:
  INC SI ;Update pointer
ADD AX, BX
  Few instructions have a label—usually marks a jump to point
  Not all instructions need a comment

## Slide 18: x86 memory accesses
# bytes from memory usually = # bytes in register
Example: MOV AX, [0x100]
  AX is 16-bit register  copy word from address 0x100 to AX
Sometimes necessary to specify size
  Use “<size> PTR”: BYTE PTR, WORD PTR, DWORD PTR
  Example: MOVZX EAX, BYTE PTR [0x100]
    Take byte from memory
    Zero-extend data to 32 bits and store in EAX
Remember, x86 uses little-endian data

## Slide 19: Final notes
Next time:
  Data transfer instructions
Reminders:
  HW 1 due Monday, 9/16
    Submit work via Blackboard
    Can handwrite solution but must scan all pages and combine into single document
      Word doc or PDF, no archive files