## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2017
Lecture 10:
PIC instruction set (continued)
Exam 2 Preview

## Slide 2: Lecture outline
Announcements/reminders
  HW 4 due 1:00 PM today
  Exam 2: Monday, 6/12
    Will again be allowed one 8.5” x 11” note sheet, calculator
    Instruction list to be provided
  PICkits to be handed out soon
    May work in groups of up to 3 or work solo
Review
  PIC instruction set basics
  Data transfers
  Bit manipulation instructions
Today’s lecture
  Logical instructions
  Shift/rotate instructions
  Program control instructions

## Slide 3: Review: PIC instructions
Four typical instruction formats (+ few special purpose)
  Upper bits of all hold opcode
  Byte-oriented includes 1 bit destination, 7 bit direct address
  Bit-oriented includes 3 bit position (0-7), 7 bit direct address
  Literal/control includes 8 bit literal
  CALL/GOTO includes 11 bit literal
Variable declarations
  cblock <start_address>: start of variable declarations
  All names between cblock/endc directives assigned to consecutive bytes starting at <start_address>

## Slide 6: Review: PIC instructions (cont.)
Clearing register: clrw/clrf
Moving values: movlw/movwf/movf
Swap nibbles: swapf
Single bit manipulation: bsf/bcf

## Slide 7: Review: Increment/Decrement/ Complement
Examples:
incf TEMP1, F ;Increment TEMP1
incf TEMP1, W ;W <- TEMP1+1; TEMP1 unchanged
decf TEMP1, F ;Decrement TEMP1
comf TEMP1, F ;Change 0s and 1s to 1s and 0s
incf f, F(W) ; increment f, putting result in F or W
decf f, F(W) ;decrement f, putting result in F or W
comf f, F(W) ;complement f, putting result in F or W
STATUS bits:
Z

## Slide 8: Review: Addition/Subtraction
Examples:
addlw 5 ; W = 5+W
addwf TEMP1, F ; TEMP1 = TEMP1+W
sublw 5 ; W = 5-W (not W = W-5 )
subwf TEMP1, F ; TEMP1 = TEMP1 - W
addlw k ;add literal value k into W
addwf f, F(W) ;add w and f, putting result in F or W
addwfc f, F(W) ;add w, f, and C, putting result in F or W
sublw k ;subtract W from literal value k, putting
;result in W
subwf f, F(W) ;subtract W from f, putting result in F or W
subwfb f, F(W) ;subtract f – W – (~C), putting result in F or W
STATUS bits:
C, DC, Z

## Slide 9: Multi-bit Manipulation
Examples:
andlw B’00000111’ ;force upper 5 bits of W to zero
andwf TEMP1, F ;TEMP1 <- TEMP1 AND W
andwf TEMP1, W ;W <- TEMP1 AND W
iorlw B’00000111’ ;force lower 3 bits of W to one
iorwf TEMP1, F ;TEMP1 <- TEMP1 OR W
xorlw B’00000111’ ;complement lower 3 bits of W
xorwf TEMP1, W ;W <- TEMP1 XOR W
andlw k ; AND literal value k into W
andwf f, F(W) ; AND W with f, putting result in F or W
iorlw k ; Inclusive-OR literal value k into W
iorwf f, F(W) ; Inclusive-OR W with f, putting result in F or W
xorlw k ; Exclusive-OR literal value k into W
xorwf f, F(W) ; Exclusive-OR W with f, putting result in F or W
STATUS bits:
Z

## Slide 10: Shift/Rotate
asrf f, F(W) ; copy f into F or W; shift F or W right one bit, keeping
; sign intact; shift LSB into C
lsrf f, F(W) ; copy f into F or W; shift F or W right one bit, shifting
; 0 into MSB; shift LSB into C
lslf f, F(W) ; copy f into F or W; shift F or W left one bit, shifting
; 0 into LSB; shift MSB into C
rlf f, F(W) ; copy f into F or W; rotate F or W left through
; the carry bit
rrf f, F(W) ; copy f into F or W; rotate F or W right through
; the carry bit
STATUS bits:
C

## Slide 11: Example
Show the values of all changed registers after the following sequence
Assume the carry bit is initially 0
cblock 0x40
z
endc
clrf z
movlw 0xF0
iorwf z, F
xorlw 0xFF
rrf z, F
andwf z, W
lslf z, F
asrf z, F

## Slide 12: Example solution
clrf z  z = 0
movlw 0xF0  W = 0xF0
iorwf z, F  z = z OR W = 0xF0
xorlw 0xFF  W = W XOR 0xFF
= 0xF0 XOR 0xFF
= 0x0F
rrf z, F  Rotate z right thru carry
Before rotate, (z, carry) = 1111 0000 02
 z = 0111 10002 = 0x78, C = 0
andwf z, W  W = z AND W
= 0x78 AND 0x0F = 0x08
lslf z, F  Shift z left
Before shift, z = 0111 10002
 z = 1111 00002 = 0xF0, C = 0
asrf z, F  Arithmetic shift right
z = 1111 10002 = 0xF8, C = 0

## Slide 13: Control flow
Examples:
goto There ; Next instruction to be executed is labeled “There”
call Task1 ; Push return address; Next instruction to be
; executed is labeled “Task1”
return ; Pop return address off of stack
retlw 5 ; Pop return address; W <- 5
retfie ; Pop return address; re-enable interrupts
goto label ; Go to labeled instruction
bra label ; Go to labeled instruction
brw ; Relative branch using W as offset
call label ; Call labeled subroutine
callw ; Subroutine call using W as address
return ; Return from subroutine
retlw k ; Return from subroutine, putting literal
; value in W
retfie ; Return from interrupt service routine;
; re-enable interrupts
STATUS bits:
none

## Slide 14: Conditional Execution
Examples:
btfsc TEMP1, 0 ; Skip the next instruction if bit 0 of TEMP1 equals 0
btfss STATUS, C ; Skip the next instruction if C==1
decfsz TEMP1, F ; Decrement TEMP1, skip if TEMP1==0
incfsz TEMP1, W ; W <- TEMP1+1 , skip if W==0 (TEMP1==0xFF)
; Leave TEMP1 unchanged
btfsc f, b ;Test bit b of register f, where b=0 to 7, skip if clear
btfss f, b ;Test bit b of register f, where b=0 to 7, skip if set
decfsz f, F(W) ;decrement f, putting result in F or W, skip if zero
incfsz f, F(W) ;increment f, putting result in F or W, skip if zero
STATUS bits:
none
Conditional execution in PIC: skip next instruction if condition true
Two general forms
  Test bit and skip if bit clear/set
  Increment/decrement register and skip if result is 0

## Slide 15: Example
Show the values of all changed registers after each of the following sequences
  What high-level operation does each perform?
(a) movf a, W
sublw 0x1A
btfsc STATUS, Z
goto L1
incf b, W
goto L2
L1
decf b, W
L2
movwf a
(b) movf NUM2, W
subwf NUM1, W
btfss STATUS, C
goto BL
movf NUM1, W
goto Done
BL
movf NUM2, W
Done
movwf MAX

## Slide 16: Example solution (part a)
movf a, W  W = a
sublw 0x1A  W = 0x1A – a
btfsc STATUS, Z  Skip goto if result
is non-zero
goto L1  Goto L1 if result == 0
 Reach this point if
result non-zero
incf b, W  W = b + 1
goto L2
L1
decf b, W  W = b - 1
L2
movwf a  a = W  value depends
on what’s executed before this
High-level operation:
if (a == 0x1A)
a = b – 1
else
a = b + 1

## Slide 17: Example solution (part b)
movf NUM2, W  W = NUM2
subwf NUM1, W  W = NUM1 – W
= NUM1 – NUM2
btfss STATUS, C  Carry indicates borrow of 0
 if set, NUM1 >= NUM2
goto BL
movf NUM1, W  if (NUM1 >= NUM2)
W = NUM1
goto Done  Skip “below” section
BL
movf NUM2, W  if (NUM1 < NUM2)
W = NUM2
Done
movwf MAX
High-level operation:
if (NUM1 >= NUM2)
MAX = NUM1
else
MAX = NUM2

## Slide 18: Exam 2 notes
Allowed
  One 8.5” x 11” double-sided sheet of notes
  Calculator
No other notes or electronic devices (phone, laptop, etc.)
Exam will last 2 hours and 20 minutes
Covers lectures 6-10
Format similar to previous exam
  1 multiple choice question
  2-3 short problems to solve/code sequences to evaluate

## Slide 19: Review: compare
CMP D, S
  Flags show result of (D) – (S)
Condition codes: mnemonics implying certain flag conditions

## Slide 20: Review: conditional instructions
Conditional move
  Move performed only if condition is true
SETcc D
  Sets single byte destination to 1 (01H) if condition true; all 0s (00H) if condition false
  Can be used to build up complex conditions

## Slide 21: Review: jump, loop
Two general types of jump
  Unconditional: JMP <target>
    Always go to target address
  Conditional: Jcc <target>
    Go to target address if condition true
Loop instructions
  Combines CX decrement with JNZ test
  May add additional required condition
    LOOPE/LOOPZ: loop if ((CX != 0) && (ZF == 1))
    LOOPNE/LOOPNZ: loop if (CX != 0) && (ZF == 0))

## Slide 22: Review: subroutines
Subroutines: low-level functions
  When called, address of next instruction saved
    Return instruction ends routine; goes to that point
  May need to save state on stack
x86 specifics
  CALL <proc>: call procedure
    <proc> can be label (16-/32-bit imm), reg, mem
  RET: return from procedure
  Saving state to stack: push instructions
    Store data “above” current TOS; decrement SP
    Basic PUSH stores word or double word
    Directly storing flags: PUSHF
    Storing all 16-/32-bit general purpose registers: PUSHA/PUSHAD
  Restoring state: POP/POPF/POPA/POPAD

## Slide 23: Review: HLL  assembly
Data accesses
  Global variables  static; allocated in data segment
  Other variables  dynamic; allocated on stack
  Stack frame for each function contains (from top)
    Saved variables within function
    Local variables for function (starting at EBP – 4)
    Saved EBP
    Saved EIP
    Function arguments (starting at EBP + 8)
Conditional statements (if-then-else)
  Evaluate condition (CMP instruction(s))
  Conditional jump (often to “else” case)
  “If” case ends with unconditional jump to skip “else”
Loops
  Initialize variable at start
  Test loop condition (similar to if)
  Change loop variable

## Slide 24: Review: PIC instructions
Four typical instruction formats (+ few special purpose)
  Upper bits of all hold opcode
  Byte-oriented includes 1 bit destination, 7 bit direct address
  Bit-oriented includes 3 bit position (0-7), 7 bit direct address
  Literal/control includes 8 bit literal
  CALL/GOTO includes 11 bit literal
Variable declarations
  cblock <start_address>: start of variable declarations
  All names between cblock/endc directives assigned to consecutive bytes starting at <start_address>

## Slide 27: Review: PIC instructions (cont.)
Clearing register: clrw/clrf
Moving values: movlw/movwf/movf
Swap nibbles: swapf
Single bit manipulation: bsf/bcf
Unary operations: incf/decf/comf
Arithmetic: addlw/addwf/addwfc/
sublw/subwf/subwfb

## Slide 28: Review: PIC instructions (cont.)
Logical operations
  andlw/andwf
  iorlw/iorwf
  xorlw/xorwf
Rotates/shifts
  rrf/lsrf/asrf
  rlf/lslf
Jumps/calls/return
  goto/bra
  call
  return/retlw/retfie
Conditional execution
  Test bit and skip next instruction if clear/set: btfsc/btfss
  Increment/decrement register and skip next instruction if zero: incfsz/decfsz
Example use: combined with goto to create conditional jump

## Slide 29: Final notes
Next time:
  Exam 2
Reminders:
  HW 4 due 1:00 PM today
  Exam 2: Monday, 6/12
    Will again be allowed one 8.5” x 11” note sheet, calculator
    Instruction list to be provided
  PICkits to be handed out soon
    May work in groups of up to 3 or work solo