## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2017
Lecture 4:
Logical instructions
Shift and rotate instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 2 due 1:00 PM today
  Exam 1 on Thursday, 5/25
    Will be allowed one double-sided 8.5” x 11” note sheet, calculator
    No other electronic devices allowed
    Instruction list provided (see website)
Review
  Arithmetic instructions
Today’s lecture
  Logical, shift, and rotate instructions

## Slide 3: Review: addition and subtraction
Reviewed flags: CF, AF, SF, ZF, PF, OF
Addition instructions
  ADD AX,BX  AX = AX + BX
  ADC AX,BX  AX = AX + BX + CF
  INC AX  AX = AX + 1
Subtraction instructions
  SUB AX,BX  AX = AX – BX
  SBB AX,BX  AX = AX – BX – CF
  DEC AX  AX = AX – 1
  NEG AX  AX = -AX = 0 - AX

## Slide 4: Review: MUL/IMUL
MUL S  unsigned multiplication
IMUL S  signed multiplication
Byte: (AX) = (AL) * (S)
Word: (DX,AX) = (AX) * (S)
Double-word: (EDX,EAX) = (EAX) * (S)
Only CF, OF updated
  If upper half of result = 0, CF & OF = 0
  Otherwise, CF & OF = 1

## Slide 5: Review: DIV/IDIV
DIV S  unsigned division
IDIV S  signed division
Result split into quotient, remainder
Byte: (AL) = (AX) / (S)
(AH) = (AX) % (S)
Word: (AX) = (DX,AX) / (S)
(DX) = (DX,AX) % (S)
Dword: (EAX) = (EDX,EAX) / (S)
(EDX) = (EDX,EAX) % (S)
Flags undefined
  Overflow causes exception

## Slide 6: Logical instructions (+ shift, rotate)
AND
OR
XOR
NOT
SAL/SHL
SHR
SAR
SHLD
SHRD
ROL
ROR
RCL
RCR

## Slide 7: AND / OR / XOR / NOT
All logical operations use form: <op> D, S 
(D) = (D) <op> (S)
  May have one memory operand
  Source may be immediate
Flags updated: CF, OF, SF, ZF, PF
  CF, OF always set to 0
AND  Logical AND
OR  Logical inclusive-OR
XOR  Logical exclusive-OR
NOT  Logical NOT

## Slide 8: Logical instructions: example
Show the state of AL after each instruction in the following sequence:
  MOV AL, 0x55
  AND AL, 0x1F
  OR AL, 0xC0
  XOR AL, 0x0F
  NOT AL

## Slide 9: Logical instructions: solution
Show the state of AL after each instruction
  MOV AL, 0x55
    AL = 0x55
  AND AL, 0x1FH
    AL = 0x55 AND 0x1F = 01010101 AND 00011111
    = 00010101 = 0x15
  OR AL, 0xC0
    AL = 0x15 OR 0xC0 = 00010101 OR 11000000
    = 11010101 = 0xD5
  XOR AL, 0x0F
    AL = 0xD5 XOR 0x0F = 11010101 XOR 00001111
    = 11011010 = 0xDA
  NOT AL
    AL = NOT 0xDA = NOT(11011010) = 00100101 = 0x25

## Slide 10: SHL / SAL / SHR / SAR
Shift instruction format: <op> D, <shamt>
  Destination may be register/memory
  <shamt>: shift amount
    May be immediate or register CL
All shift instructions store last bit shifted out in carry flag (CF)
SHL: logical shift left (double-precision version SHLD)
SAL: arithmetic shift left
  Shift to left by <shamt> bits; shift 0s into LS bits
SHR: logical shift right (double-precision version SHRD)
  Shift to right by <shamt> bits; shift 0s into MS bits
SAR: arithmetic shift right
  Shift to right by <shamt> bits; copy original MSB to fill MS bits (keep sign of value intact)

## Slide 11: SAL/SHL example
SHL AX,1
Before execution
  Dest = (AX) = 0x1234 = 0001 0010 0011 01002 ,
  Count = 1, CF = X
Operation
  The value in all bits of AX are shifted left one bit position
  Emptied LSB is filled with 0
  Value shifted out of MSB goes to carry flag
After execution
  Dest = (AX) = 0x2468 = 0010 0100 0110 10002 , CF = 0
Notes
  MSB isolated in CF; can be used by conditional instruction
  Result has been multiplied by 2

## Slide 12: SHR example
SHR AX,CL
Before execution
  Dest = (AX) = 0x1234 = 466010 = 0001 00100011 01002
  Count = (CL) = 0x02 , CF = X
Operation
  The value in all bits of AX are shifted right two bit positions
  Emptied MSBs are filled with 0s
  Values shifted out of LSBs go to carry flag
After execution
  Dest = (AX) = 0x048D = 116510 = 0000 0100 1000 11012 ,CF = 0
Notes:
  Bit 1 isolated in CF
  Result has been divided by 4
    4 X 1165 = 4660

## Slide 13: SAR example
SAR AX,CL
Before execution
  Dest = (AX) = 0x091A = 00001001000110102 = +2330, Count = 0x02 , CF = X
Operation
  The value in all bits of AX are shifted right two bit positions
  Emptied MSB is filled with the value of the sign bit—sign maintained
  Values shifted out of LSBs go to carry flag
After execution
  Dest = (AX) = 0x0246 = 00000010010001102 = +582 , CF = 1
Conclusion
  Bit 1 isolated in CF
  Result has been sign extended
  Result value has been divided by 4 and rounded to integer
    4 X +582 = +2328

## Slide 14: Shift example
Example: Given AL = 0x15, CL = 0x03, and CF = 0 show the state of AL and CF after each instruction in the sequence below:
  SHL AL, 1
  SHR AL, CL
  SAL AL, 5
  SAR AL, 2

## Slide 15: Solution
Initially, AL = 0x15 = 000101012
SHL AL, 1
  AL = (00010101 << 1) = 001010102 = 0x2A
  CF = last bit shifted out = 0
SHR AL, CL
  AL = (00101010 >> 3) = 000001012 = 0x05
  CF = last bit shifted out = 0
SAL AL, 5
  “Arithmetic” left shift same as SHL
  AL = (00000101 << 5) = 101000002 = 0xA0
  CF = last bit shifted out = 0
SAR AL, 2
  Arithmetic right shift keeps sign intact—copy MSB to fill leftmost positions
  AL = (10100000 >> 2) = 111010002 = 0xE8
  CF = last bit shifted out = 0

## Slide 16: Rotate instructions
Difference between rotates and shifts
  Shifts discard bits that are shifted out
  Rotates take bits that are shifted out and use them to fill vacated bits
Rotate instruction format: <op> D, <shamt>
  Destination may be register/memory
  <shamt>: shift amount
    May be immediate or register CL
All rotate instructions store last bit shifted out in carry flag (CF)

## Slide 17: ROR / ROL / RCR / RCL
ROR: rotate right
  Shift (D) to right by <shamt> bits
  <shamt> LS bits are moved to MS bits
ROL: rotate left
  Shift (D) to left by <shamt> bits
  <shamt> MS bits are moved to LS bits
RCR: rotate right through carry
  Treat (CF) as extra LS bit
  Shift (D,CF) to right by <shamt> bits
  <shamt> LS bits (from (D,CF)) are moved to MS bits
RCL: rotate left through carry
  Treat (CF) as extra MS bit
  Shift (CF,D) to left by <shamt> bits
  <shamt> MS bits (from (CF,D)) are moved to LS bits

## Slide 18: ROL example
ROL AX,1
Before execution
  Dest = (AX) = 0x1234 = 0001 0010 0011 01002
  Count = 1, CF = 0
Operation
  The value in all bits of AX are rotated left one bit position
  Value rotated out of the MSB is reloaded at LSB
  Value rotated out of MSB copied to carry flag
After execution
  Dest = (AX) = 0x2468 = 00100100011010002
  CF = 0

## Slide 19: ROR example
ROR AX,CL
Before execution
  Dest = (AX) = 0x1234 = 0001 0010 0011 01002
  Count = 0x04, CF = 0
Operation
  The value in all bits of AX are rotated right four bit positions
  Values rotated out of the LSB are reloaded at MSB
  Values rotated out of MSB copied to carry flag
After execution
  Dest = (AX) = 0x4123 = 01000001001000112
  CF = 0
Note position of hex characters in AX have been rearranged

## Slide 20: RCL example
RCL BX,CL
Before execution
  Dest = (BX) = 0x1234 = 0001 0010 0011 01002
  Count = 0x04, CF = 0
Operation
  The value in all bits of AX are shifted left four bit positions
  Emptied MSBs are rotated through the carry bit back into the LSB
  Last value rotated out of MSB retained in carry flag
  First rotate loads prior value of CF at the LSB
After execution
  Dest = (BX) = 0x2340 = 0010 0011 0100 00002
  CF = 1

## Slide 21: Rotate example
Given AL = 0x43, CL = 0x04, and CF = 0, show the state of AL after each instruction in the sequence below:
  ROR AL, 2
  ROL AL, CL
  RCR AL, 3
  RCL AL, 4

## Slide 22: Solution
Initially, AL = 0x43 = 010000112
ROR AL, 2
  AL = 01000011 rotated right by 2
  = 11010000 = 0xD0
  CF = last bit rotated in = 1
ROL AL, CL
  AL = 11010000 rotated left by 4
  = 00001101 = 0x0D
  CF = last bit rotated in = 1

## Slide 23: Solution (cont.)
RCR AL, 3
  (AL,CF) = 00001101 1 rotated right by 3
  = 01100001 1
  CF = 1, AL = 011000012 = 0x61
RCL AL, 4
  (CF,AL) = 1 01100001 rotated left by 4
  = 0 00011011
  CF = 0, AL = 000110112 = 0x1B

## Slide 24: Final notes
Next time:
  Bit test and bit scan instructions
  Exam 1 Preview
Reminders:
  HW 2 due 1:00 PM today
  Exam 1 on Thursday, 5/25
    Will be allowed one double-sided 8.5” x 11” note sheet, calculator
    No other electronic devices allowed
    Instruction list provided (see website)