## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2017
Lecture 5:
Bit test and bit scan instructions
Exam 1 Preview

## Slide 2: Lecture outline
Announcements/reminders
  Exam 1: Thursday, 5/25
    Allowed calculator, one double-sided 8.5” x 11” note sheet
    Will be given list of instructions covered so far
  No lecture Monday, 5/29 (Memorial Day)
Review
  Logical instructions
  Shift instructions
  Rotate instructions
Today’s lecture
  Bit test/scan instructions
  Exam 1 Preview

## Slide 3: Review: Logical instructions
Logical instructions (AND/OR/XOR/NOT)
Basic shift instructions
  Move value by <amt> bits; add 0s to left or right
  CF = last bit shifted out
  SHL <src>, <amt>: Move <src> to left
    SAL exactly the same
  SHR <src>, <amt>: Move <src> to right
Arithmetic right shift
  Move value right by <amt> bits
  Copy sign bit to fill remaining bits
  CF = last bit shifted out
  SAR <src>, <amt>

## Slide 4: Review: rotate instructions
Rotate instructions: bits that are shifted out one side are shifted back in other side
  ROL <src>, <amt> or ROR <src>, <amt>
  CF = last bit rotated
Rotate through carry instructions
  CF acts as “extra” bit that is part of value being rotated
  RCL <src>, <amt> or RCR <src>, <amt>

## Slide 5: Bit Test Instructions
BT  Bit test
BTR  Bit test and reset
BTS  Bit test and set
BTC  Bit test and complement
Format of bit test instruction: BT(x) D,S
  (S)  index that selects the position of the bit tested
  (D)  Holds value tested
Operation:
  Enables programmer to test bit in a value in register or memory
  All  Save the value of the selected bit in the CF
  BT  Leaves selected bit unchanged
  BTR  Clears the bit (bit = 0)
  BTS  Sets the bit (bit = 1)
  BTC  Complements the bit (bit = ~bit)

## Slide 6: Bit Test Instructions
Example:
  BTC BX,7
Before execution
  (BX) = 03F0H = 0000 0011 1111 00002
After Execution
  (CF) = bit 7 of BX = 1
  (BX) = 0370H = 0000 0011 0111 00002

## Slide 7: Bit Scan Instructions
BSF  Bit scan forward
BSR  Bit scan reverse
Format of bit scan instructions: BS(x) D,S
  (S)  Holds value for which bits are tested to be 0
  (D)  Index of first bit that tests as non-zero
Operation:
  Enable programmer to test value to determine if all bits are 0
  BSF  Scans bits starting from bit 0
    Set ZF = 0 if all bits are found to be zero
    Sets ZF = 1 when first 1 bit detected and places index of that bit into destination
  BSR  Scans bits starting from MSB
    Set ZF = 0 if all bits are found to be zero
    Sets ZF = 1 when first 1 bit detected and places index of that bit into destination
Example:
  BSF ESI,EDX  32-bits of EDX scanned starting from B0
  If EDX = 00000000  ZF = 0 (all bits zero)
  If EDX = 00000001  ESI = 00000000, ZF = 1 (bit 0 is 1)
  If EDX = 00003000  ESI = 0000000C, ZF = 1 (bit 12 is first bit set to 1)

## Slide 8: Example
Given initial state shown in handout
List all changed registers/memory locations and their values, as well as CF
Instructions
  BT WORD PTR [21102h], 4
  BTC WORD PTR [21110h], 1
  BTS WORD PTR [21104h], 1
  BSF CX, WORD PTR [2110Eh]
  BSR DX, WORD PTR [21109h]

## Slide 9: Example solution
BT WORD PTR [21102h], 4
  Word at 21102 = 1010h = 0001 0000 0001 0000
  CF = bit 4 = 1
BTC WORD PTR [21110h], 1
  Word at 21110 = 001Eh = 0000 0000 0001 1110
  CF = bit 1 = 1
  Complement bit 1
    Word at 21110 = 0000 0000 0001 1100 = 001Ch

## Slide 10: Example solution (cont.)
BTS WORD PTR [21104h], 1
  Word at 21104 = 0189h = 0000 0001 1000 1001
  CF = bit 1 = 0
  Set bit 1
    Word at 21110 = 0000 0001 1000 1011 = 018BH
BSF CX, WORD PTR [2110Eh]
  Word at 2110E = 00FFh = 0000 0000 1111 1111
  Word is not zero  ZF = 1
  First non-zero bit (starting from bit 0) is bit 0  CX = 0000h
BSR DX, WORD PTR [21109h]
  Word at 2110E = 0000h = 0000 0000 0000 0000
  Word is zero  ZF = 0
  DX unchanged

## Slide 11: Exam 1 notes
Allowed
  One 8.5” x 11” double-sided sheet of notes
  Calculator
x86 instruction set (so far) provided for you
No other notes or electronic devices (phone, laptop, etc.)
Exam will be 2 hours and 20 minutes
  Will start at 10:30—please be on time!
Covers all lectures through Monday
General format
  1 multiple choice question
  2-3 short answer questions
  1 extra credit problem

## Slide 12: Test policies
Prior to passing out exam, I will verify that you only have one note sheet
  If you have multiple sheets, I will take all notes
You will not be allowed to remove anything from your bag after that point in time
  If you need an additional pencil, eraser, or piece of scrap paper during the exam, ask me
Only one person will be allowed to use the bathroom at a time
  You must leave your cell phone either with me or clearly visible on the table near your seat

## Slide 13: Review: ISA, storage
Instruction set architecture (cont.)
  Operands: the data being operated on
    How are the bits interpreted? (int, FP, signed/unsigned)
    What size are they? (byte, word, etc.)
    How do we reference operands?
Data storage
  Registers
    Small, fast set of on-chip storage (primarily for speed)
    Referenced by name
  Memory
    Larger, slower set of storage (primarily for capacity)
    Organized as hierarchy …
    … but programmer references single range of addresses
    Memory issues
      Aligned data: address divisible by number of bytes
      Endianness: 80x86 data is little endian

## Slide 14: Review: data & data transfer instructions
x86 data
  Registers: access as 8-bit (e.g. AL, AH), 16-bit (AX), 32-bit (EAX)
  Memory
    Data size usually matches register
    If not, explicitly specify (BYTE PTR, WORD PTR, DWORD PTR)
MOV: basic data transfer
  Can use registers, memory, immediates
MOVSX/MOVZX
  Sign-extend or zero-extend register/memory value
XCHG
  Exchange contents of source, dest

## Slide 15: Review: data transfer, arithmetic
LEA: load effective address
  Calculate EA/store in register
Reviewed flags: CF, AF, SF, ZF, PF, OF
Addition instructions
  ADD AX,BX  AX = AX + BX
  ADC AX,BX  AX = AX + BX + CF
  INC AX  AX = AX + 1
Subtraction instructions
  SUB AX,BX  AX = AX – BX
  SBB AX,BX  AX = AX – BX – CF
  DEC AX  AX = AX – 1
  NEG AX  AX = -AX = 0 - AX

## Slide 16: Review: Multiplication & division
Multiplication instructions
  MUL (unsigned), IMUL (signed)
  Result uses 2x bits of source
  Source usually implied (AL/AX/EAX)
Division instructions
  DIV (unsigned), IDIV (signed)
  Implied source (AX, (DX,AX), (EDX,EAX)) 2x bits of specified source
  Quotient/remainder split across result

## Slide 17: Review: Logical instructions
Logical instructions (AND/OR/XOR/NOT)
Basic shift instructions
  Move value by <amt> bits; add 0s to left or right
  CF = last bit shifted out
  SHL <src>, <amt>: Move <src> to left
    SAL exactly the same
  SHR <src>, <amt>: Move <src> to right
Arithmetic right shift
  Move value right by <amt> bits
  Copy sign bit to fill remaining bits
  CF = last bit shifted out
  SAR <src>, <amt>

## Slide 18: Review: rotate instructions
Rotate instructions: bits that are shifted out one side are shifted back in other side
  ROL <src>, <amt> or ROR <src>, <amt>
  CF = last bit rotated
Rotate through carry instructions
  CF acts as “extra” bit that is part of value being rotated
  RCL <src>, <amt> or RCR <src>, <amt>

## Slide 19: Final notes
Next time:
  Exam 1
Reminders:
  No lecture Monday, 5/29 (Memorial Day)