## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2016
Lecture 6:
Conditional execution
Jump/loop instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 3 to be posted; due Monday, 6/5
Today’s lecture
  Conditional execution
  Jump/loop instructions

## Slide 3: Compare Instructions
Compare 2 values; store result in ZF/SF
General format: CMP D,S
  Works by performing subtraction (D) – (S)
    D, S unchanged
  ZF/SF/OF indicate result (signed values)
    ZF = 1  D == S
    ZF = 0, (SF XOR OF) = 1  D < S
    ZF = 0, (SF XOR OF) = 0  D > S
Notes: (D) (S) result CF SF AF
AX BX
2345>1234 0 0 0
1234<2345 1 1 1
1234>ABCD 1 0 1
ABCD<1234 0 1 0
ABCD>A000 0 0 0
A000<ABCD 1 1 1
7FFF 8000 overflow

## Slide 4: Condition codes
Conditional execution: result depends on value of flag bit(s)
Intel instructions specify condition codes
  Condition code implies certain flag values
  Opcodes written with cc as part of name
  cc can be replaced by any valid code
  Examples: CMOVcc, SETcc, Jcc
    Specific examples: CMOVE, SETL, SETZ, JNE, JG

## Slide 5: Condition codes (cont.)
Testing overflow
  O (OF = 1), NO (OF =0)
Testing carry flag
  C (CF = 1)
  NC (CF = 0)
Testing sign flag
  S (SF = 1), NS (SF = 0)
Testing parity flag
  P or PE (PF = 1)
  NP or PO (PF = 0)

## Slide 6: Condition codes (cont.)
Testing equality/zero result
  E or Z (ZF = 1)
  NE or NZ (ZF = 0)
Signed comparison
  L or NGE (SF XOR OF = 1)
  NL or GE (SF XOR OF = 0)
  LE or NG ((SF XOR OF) OR ZF = 1)
  NLE or G ((SF XOR OF) OR ZF = 0)
Unsigned comparison
  “Below”  less than, “above”  greater than
  B, NAE (CF = 1)
  NB, AE (CF = 0)
  BE or NA (CF OR ZF = 1)
  NBE or A (CF OR ZF = 0)

## Slide 7: Conditional move (CMOV)
Only in Pentium Pro & later
Perform move only if condition is true
Examples:
  CMOVZ AX, [SI]  move if ZF == 1
  CMOVG EBX, EAX  move if greater than

## Slide 8: Byte Set on Condition Instruction
Byte set on condition instruction
  Used to set byte based on condition code
  Can be used for boolean results—complex conditions
  General format:
    SETcc D
    cc = one of the supported conditional relationships
  Result
    D = 01h if condition true
    D = 00h if condition false

## Slide 9: Byte Set on Condition Instruction
Operation: Flags tested for conditions defined by “cc” and the destination in a register or memory updated as follows
If cc test True:
  000000012 = 01H  D
  If cc test False:
  000000002 = 00H  D
Examples of conditional tests:
SETE = set byte if equal  ZF = 1
SETC = set byte if carry  CF =1
SETBE = set byte if below or equal  CF = 1 +(or) ZF = 1
Example: SETA AL = set byte if above
  if CF = 0  (and) ZF = 0
  (AL) = 01H
  Otherwise,
  (AL) =00H

## Slide 10: Example
Show the results of the following instructions, assuming that
  “A” = (100H) = 0001H
  “B” = (102H) = 0003H
  “C” = (104H) = 1011H
  “D” = (106H) = 1011H
  “E” = (108H) = ABCDH
  “F” = (10AH) = DCBAH
What complex condition does this sequence test?
MOV AX, [100H]
CMP AX, [102H]
SETLE BL
MOV AX, [104H]
CMP AX, [106H]
SETE BH
AND BL, BH
MOV AX, [108H]
CMP AX, [10AH]
SETNE BH
OR BL, BH

## Slide 11: Example solution
Condition being tested:
  To simplify, treat each word as a variable named “A” through “F”
  ((A <= B) && (C == D)) || (E != F)
Source: http://www.arl.wustl.edu/~lockwood/class/cs306/books/artofasm/Chapter_6/CH06-4.html

## Slide 12: Jump instructions
Used to change flow of program
  Next instruction specified by operand
Two general types
  Unconditional: JMP <target>
    Always goes to address indicated by <target>
  Conditional: Jcc <target>
    Jump only occurs if condition true
    cc replaced by valid condition code
      Most codes discussed in previous lecture
      Additional codes: CXZ/ECXZ
       CX/ECX register is zero

## Slide 13: Jump Instructions

## Slide 14: Example: program structure 1
Given the instructions below, what are the resulting register values if:
  AX = 0010H, BX = 0010H
  AX = 1234H, BX = 4321H
What type of high-level program structure does this sequence demonstrate?
Instructions
  CMP AX, BX
  JE L1
  ADD AX, 1
  JMP L2
  L1: SUB AX, 1
  L2: MOV [100H], AX

## Slide 15: Example solution
First case: AX = BX = 0010H
  CMP AX, BX  Shows AX == BX
  JE L1  Cond. true—jump to L1
  ADD AX, 1
  JMP L2
  L1: SUB AX, 1  AX = AX – 1 = 000F
  L2: MOV [100H], AX  Store 000F at DS:100H

## Slide 16: Example solution (cont.)
Second case: AX = 1234H, BX = 4321H
  CMP AX, BX  Shows AX < BX
  JE L1  Cond. false—no jump
  ADD AX, 1  AX = AX + 1 = 1235H
  JMP L2
  L1: SUB AX, 1  AX = AX – 1 = 000F
  L2: MOV [100H], AX  Store 000F at DS:100H

## Slide 17: Example solution (cont.)
High-level program structure: if/else statement
  If part: compare + jump (if (AX == BX))
  Else part: what follows if condition false
  Unconditional jump used to skip “if” part
  Both parts have same exit (L2)

## Slide 18: Example: program structure 2
Given the instructions below, what are the resulting register values if, initially, AX = 0001H?
What type of high-level program structure does this sequence demonstrate?
Instructions
  MOV CL, 5
  L: SHL AX, 1
  DEC CL
  JNZ L

## Slide 19: Example: program structure 3
Given the instructions below, what are the resulting register values if, initially, AX = 0001H?
What type of high-level program structure does this sequence demonstrate?
Instructions
  MOV CX, 5
  L: JCXZ END
  ADD AX, AX
  DEC CX
  JMP L
  END: MOV [10H], AX

## Slide 20: Block Move Program

## Slide 21: Loop instructions
Common operations in basic loops
  Compare
  Conditional jump
  Decrement loop counter (CX)
Loop instructions combine all into one op
  All decrement CX by 1, then check if CX == 0
  <target> must be short-label (8-bit immediate)
  LOOP <target>: Return to <target> if CX != 0
  LOOPE/LOOPZ <target>: Return to <target> if (CX != 0) && (ZF == 1)
  LOOPNE/LOOPNZ <target>: Return to <target> if (CX != 0) && (ZF != 1)

## Slide 22: Loop Program Structure
Structure of a loop
  CX = initial count
  Loop body: code to be repeated
  Loop instruction– determines if loop is complete or if the body is to repeat
Example: block move

## Slide 23: Loop example 1
Rewrite the post-tested loop seen earlier using a loop instruction:
  MOV CL, 5
  L: SHL AX, 1
  DEC CL
  JNZ L
Solution:
  MOV CL, 5
  L: SHL AX, 1
  LOOP L

## Slide 24: Loop example 2
Describe the operation of the following program (Example 6.15-6.16).
What is the final value of ESI if the 15 bytes between 0A001 and 0A00F have the following values?
  00 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E
MOV DL, 05
MOV EAX, 0000A000h
MOV ESI, 00000000h
MOV CX, 000F
AGAIN:INC SI
CMP [EAX + ESI], DL
LOOPNE AGAIN

## Slide 25: Final notes
Next time:
  Subroutines
  HLL and x86 assembly
Reminders:
  HW 3 to be posted; due Monday, 65