## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2017
Lecture 7:
Subroutines
HLL  assembly

## Slide 2: Lecture outline
Announcements/reminders
  HW 3 due 1:00 PM, 6/5
Review
  Conditional execution
  Jump/loop instructions
Today’s lecture
  Subroutines
  Stack details
  HLL  assembly

## Slide 3: Review: conditional instructions
Conditional move
  Move performed only if condition is true
SETcc D
  Sets single byte destination to 1 (01H) if condition true; all 0s (00H) if condition false
  Can be used to build up complex conditions

## Slide 4: Review: jump, loop
Two general types of jump
  Unconditional: JMP <target>
    Always go to target address
  Conditional: Jcc <target>
    Go to target address if condition true
Loop instructions
  Combines CX decrement with JNZ test
  May add additional required condition
    LOOPE/LOOPZ: loop if ((CX != 0) && (ZF == 1))
    LOOPNE/LOOPNZ: loop if (CX != 0) && (ZF == 0))

## Slide 5: Subroutines
Subroutine: special program segment that can be “called” from any point in program
  Implements HLL functions/procedures
  Written to perform operation that must be repeated in program
  Actual subroutine code only written once

## Slide 6: Subroutine operation
When called, address of next instruction saved
  State may need to be saved before call
  Parameters can be passed
Control of program transferred to subroutine
After subroutine finished, return instruction goes back to saved address

## Slide 7: x86 subroutines
Specify starting point with pseudo-op
  <name> PROC
May save state/allocate variables at start
  If so, will restore at end of subroutine
Last instruction returns to saved address
  Always RET
Pseudo-op after RET indicates routine end
  <name> ENDP

## Slide 8: Subroutine example
SQUARE PROC
PUSH AX ; Save AX to stack
MOV AL, BL ; Copy BL to AL
IMUL BL ; AX = BL * AL
; = original BL squared
MOV BX, AX ; Copy result to BX
POP AX ; Restore AX
RET
SQUARE ENDP

## Slide 9: Call/return
Calling subroutine: CALL <proc>
  Address of next instruction saved on stack
    Either IP or EIP (instruction pointer)
When function ends, use return instruction (RET)
  Jumps to saved return address (IP/EIP)

## Slide 10: Example
Assuming AX = 2 and BX = 4, show the results of the following sequence:
  Assume the addresses of the first three instructions are 0005, 0008, and 0009, respectively
  CALL SUM
  RET ; End main function
  SUM PROC NEAR
  MOV DX, AX
  ADD DX, BX
  RET
  SUM ENDP

## Slide 11: Example results
  CALL SUM
  RET ; End main function
  SUM PROC NEAR
  MOV DX, AX DX = AX = 2
  ADD DX, BX DX = DX + BX = 2 + 4 = 6
  RET
  SUM ENDP

## Slide 12: Saving state
May need to save state before routine starts
  Overwritten registers (that aren’t return values)
  Flags
Placing data on stack: PUSH
  Store data “above” current TOS; decrement SP
    Stack grows toward lower addresses
    New SP points to start of data just stored
  Basic PUSH stores word or double word
  Directly storing flags: PUSHF
  Storing all 16-/32-bit general purpose registers: PUSHA/PUSHAD

## Slide 13: Restoring state
Removing data from TOS: POP
  Data removed from TOS; SP incremented
  Basic POP removes word/double word
  Directly removing flags: POPF
  Removing all 16-/32-bit general purpose registers: POPA/POPAD
POP instructions generally executed in reverse order of corresponding PUSH instructions

## Slide 14: Revisiting subroutine example
SQUARE PROC NEAR
PUSH AX ; Save AX to stack
MOV AL, BL ; Copy BL to AL
IMUL BL ; AX = BL * AL
; = original BL squared
MOV BX, AX ; Copy result to BX
POP AX ; Restore AX
RET
SQUARE ENDP

## Slide 15: Push All and Pop All Operations

## Slide 16: Stack examples
Assume initial state shown in handout
What is the resulting stack state of each of the following sequences?
  PUSH BX
  PUSH AX
  PUSH EBX
  PUSH EAX
  PUSHA

## Slide 17: Solution
What is the resulting stack state of each of the following sequences?
  PUSH BX
  PUSH AX
  4 bytes pushed to stack, so SP decremented by 4  ESP = 00001FFCH
  AX is at top of stack; BX is below that
  PUSH EBX
  PUSH EAX
  8 bytes pushed to stack, so SP decremented by 8  ESP = 00001FF8H
  EAX is at top of stack; EBX is below that
  PUSHA
  8 words = 16 bytes pushed to stack, so SP decremented by 16  ESP = 00001FF0H
  As shown in slide 13, DI is at top of stack, followed by SI, BP, old SP, BX, DX, CX, and AX

## Slide 18: HLL  assembly
Given some brief examples already; want to think about common HLL concepts and their assembly counterparts
Compiling HLL to assembly
  Data accesses
  Stack usage with function calls
  Conditional statements (if-then-else)
  Loops

## Slide 19: Sample program
int X[10], Y[10]; // integer arrays
int i, j; // index variables
for (i = 0; i < 10; i++) { // outer loop
X[i] = i * 2; // set X[i]
for (j = 0; j < 10; j++) { // inner loop
if (j < 5) // set Y[j]
Y[j] = X[i] + j; // based on
else // value of j
Y[j] = X[i] – j;
}
}

## Slide 20: Data representations
Program references four pieces of data
  Two integer arrays: X[10], Y[10]
  Two integer index variables: i, j
Compilers must account for:
  Data size: is variable a double word, word, or byte?
    Characters (char) are always 8 bits  1 byte
    Other types system-dependent
      In x86, integers (int) are 32 bits  4 bytes  double word
      Short integers (short) are 16 bits  2 bytes  word
  Data location: where is data allocated?
    Depends on how it’s allocated …
    If writing assembly by hand, static data  directly allocated in memory
    If compiled code or function call, allocated on stack
      Variables declared inside functions, function arguments

## Slide 21: Static data accesses
Global declarations in high-level program
Stored in data segment
Offset into data segment declared as symbol
Example (from testfile2.asm)
  mov eax, DWORD PTR _c

## Slide 22: Stack accesses
On function call
SP or ESP: points to current top of stack
  Lowest address in current stack frame
BP or EBP: used to reference data within frame
  Arguments
  Local variables

## Slide 23: Stack accesses (cont.)
Arguments start at offset 8 from EBP
Local variables start at offset -4 from EBP
Starting offset of each variable can be defined as symbol
Ex. (testfile1.asm) _j$ = -120; size = 4
_i$ = -108; size = 4
_Y$ = -96; size = 40
_X$ = -48; size = 40
mov DWORD PTR _i$[ebp], 0
 sets i = 0

## Slide 24: Final notes
Next time:
  More on HLL  assembly
Announcements/reminders
  HW 3 due 1:00 PM, 6/5