## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors: Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lecture 33:
PICkit introduction

## Slide 2: Lecture outline
Today’s lecture: working with PICkit
  Assembler directives
  MPLAB IDE
    Working with existing projects
    Simulator
    In-circuit debugging
  Sample programs in assembly and C

## Slide 3: PIC microcontroller programming
Done through MPLAB IDE
Allows for generation of projects in assembly or in C
Options to generate initialization code
In-circuit debugger to view device state while hardware is actually running

## Slide 4: PIC assembler directives
banksel label
  Changes BSR to bank containing label
  Example: banksel TRISC
cblock/endc
  Used to define a block of variables
org address
  Indicates starting address for block of code that follows
  Address 0 in simple programs (initial PC value)
#include file
  Typically used to include processor-specific definitions, macros

## Slide 5: Example 1: Light single LED (.asm)
Start:
banksel TRISC ;select bank1
bcf TRISC,0 ;make C0 an output
banksel LATC ;select bank2
clrf LATC ;initialize the
; LATCH by
; turning off
; everything
bsf LATC,0 ;turn on LED C0 (DS1)
goto $ ;sit here forever!
end

## Slide 6: Example 1 notes (.asm)
TRISC: controls state of Port C pins
  TRISC bits = 1  corresponding pins are inputs
  TRISC bits = 0  corresponding pins are outputs
LATC: used for writing data to Port C
  Equivalent to writing to PORTC register
  Convention: for input, read PORTC; for output, write LATC
Infinite loop at end
  $ symbol—special label for current instruction

## Slide 7: Example 1: Light single LED (C)
void main(void) {
TRISCbits.TRISC0 = 0; // Pin 0 =
// output
LATC = 0; //clear all pins to 0
LATCbits.LATC0 = 1; // turn ON LED
while(1) continue;
}

## Slide 8: Example 1 notes (C)
Can access entire registers by name
To access individual bits, use form:
regnamebits.regname#
  Example: TRISCbits.TRISC0 = 0;

## Slide 9: Running program
Choose target device under
File  Project Properties
  Either use PICkit3 or Simulator
Compilation
  Clean and Build
  Make and Program Device (PICkit3 only)
    Separate options required for debug configuration
    Click arrow on right of button to build/make for debug
Window  PIC Memory Views
  Allows you to view file registers and/or SFRs

## Slide 10: Final notes
Next time:
  Working with delay